## Slide 1: MRP Pyomo Model ? Functional Overview
Inputs, optimization logic, and outputs

## Slide 2: Agenda
Model scope and flow
Optimization logic (multi?phase objective)
Inputs (Excel / JSON)
Outputs (Excel results)
Resource consumption reporting

## Slide 3: Model Scope
Multi?product, multi?location, multi?period MRP
Make, buy, and transfer decisions
BOM?driven dependent demand
Resource?based production capacity
Lead times and lot sizing

## Slide 4: Core Flow
Independent demand enters at product/location/period
Dependent demand from BOM is created by production releases
Inventory balance tracks receipts, demand, and transfers
Transfers move stock across locations with lead time

## Slide 5: Optimization Logic
Phase A: Minimize total backlog
Phase B: Minimize total inventory (given best backlog)
Phase C: Minimize total buy volume (given backlog & inventory)
Phase D: Minimize transfer usage weighted by lane priority

## Slide 6: Key Constraints
Inventory balance (per product/location/period)
Resource capacity (sum of routed production)
Make/Buy permissions via procurement type
Lead times for make, buy, and transport
Lot sizing (min lot + multiple)
Transfer lane allow, capacity, and lead time

## Slide 7: Inputs ? Excel Tabs
Time_periods, Locations, Products
Proc_Type, Resources, Routing
Resource_Capacity, Purchasing_Capacity
BOM (includes lt_make, min/multiple lot make)
Purchasing (leadtime, min/mult lotsize)
TransportationLanes, Transportation_Capacity
Initial_Inventory, Independent_Demand

## Slide 8: Inputs ? JSON (auto?generated)
JSON mirrors the Excel tabs
BOM rows + purchasing rows + transportation lanes
Used as fallback if Excel is missing

## Slide 9: Outputs ? Excel
Result sheet: key figures as rows, periods as columns
Includes demand, dep demand, ship out/in, receipts, SOH
Resource_Consumption: totals by resource/location/period
Resource_Consumption_Detail: by resource/location/product

## Slide 10: Resource Consumption
Calculated as SUM(Production ? Routing usage)
Reported per resource/location/period
Detail sheet shows product/location contribution

## Slide 11: Execution Flow
Read input.xlsx (default); write data.json for traceability
Build and solve model in Pyomo
Write result Excel with timestamp